## Slide 1
1
CHAPTER 5.4.
MOBILITY AWARE SENSING DESIGN
S. Cacciapuoti, I. F. Akyildiz and L. Paura,
“Optimal Primary-User Mobility Aware Spectrum Sensing Design for Cognitive Radio Networks”,
IEEE Journal on Selected Areas in Communications, Nov. 2013.

## Slide 2: Optimal Primary-User Mobility Aware Sensing Design: Overview
2
  Spectrum sensing functionality by jointly
    maximizing the sensing efficiency
    satisfying the PU interference constraint
  in presence of Primary-User mobility.

## Slide 3: Conventional Sensing Scenarios
3
Large-Scale PU Networks
    Static PUs
    CR users are always inside the PU range
      Their capability to sense the PU transmissions does not vary in time

## Slide 4: Our Considered Sensing Scenarios
4
Small-Scale PU Networks
    Mobile PUs
    CR users can be out of the PU range
      Their capability to sense the PU transmissions varies in time

## Slide 5: Why Small-Scale PU Networks?
5
  Gained a lot of attention recently
  Examples of small-scale PU networks:
    Ad hoc networks
    Wireless personal area networks
    HetNets (Small Cells)
    Wireless microphones

## Slide 6: Why focus on Spectrum Sensing?
6
  Mobility changes dynamically the mutual distances among PUs and CR users
    CR capability to sense the PU transmission varies in time
    An effective sensing must be aware of the mobile PU dynamics

## Slide 7: Example: Impact of PU Mobility on Sensing
7
t
time
At time t the CR user is out
of the PU range
  it cannot sense the PU transmissions
After the PU movement, the
CR user is inside the PU range
  it can sense the PU transmissions

## Slide 8: Objectives
8
IN MOBILE PU SCENARIOS:
Maximize the Sensing Efficiency
Satisfy the PU Interference Avoidance

## Slide 9: How?
9
Tuning the sensing time and the transmission time
according to the mobile PU dynamics:
    How often must the sensing be performed in presence of PU mobility?
    How long must a spectrum band be sensed to reliably detect mobile PUs?

## Slide 10: Why?
10
  Sensing time and transmission time influence both the spectrum
  efficiency and interference avoidance.
  Proper selection of these parameters is the most critical factor
  influencing the performance of CR networks.

## Slide 11: Example: Transmission Time
Hypothesis: Ideal Sensing
  Static scenarios  no interference
  Mobile Scenarios  the interference can be greater than zero
    At the end of the sensing time Ts, CR user correctly decides to use the band
    At t0,an active PU arrives during the CR transmission time
    CR user interferes with the PU, despite the perfect sensing decision
11
Notes: At the end of the sensing time Ts, the CR user correctly decides to use the monitored spectrum band, since it does not detect any PU transmission during the sensing time. However, at time t_0 in TTx a mobile PU enters in the CR range. As a consequence, if the PU is active, the CR user interferes the PU, despite the perfect sensing decision.

## Slide 12: Example: Sensing Time
Static Scenarios:
  A CR user is always inside the PU range  Sensing is mandatory
Mobile Scenarios:
  A CR user can be out of the PU range
  If the prob of being inside the PU range is lower than the maximum interference prob tolerated by the PU
   Sensing is useless
    Sensing time should be set equal to zero since the CR prob to interfere the PU is lower than the PU interference constraint.
12

## Slide 13: CONTRIBUTIONS
13
1. Optimal transmission time for a general mobility model
Jointly maximize the sensing efficiency and satisfies the PU interference constraint.
2. Proof of a threshold behavior in the sensing accuracy as a function of the sensing time:
in mobile scenarios the sensing accuracy decreases for [sensing times > threshold value]
SURPRISE !!!!!
In static scenarios:
longer sensing times  higher sensing accuracy  less interference

## Slide 14: CONTRIBUTIONS
14
3. Closed-form expression of the optimal sensing time threshold
for a general mobility model
4. Practical rules for setting the transmission time and the sensing time when
the PUs move according to Random Walk Mobility Model (RWM)
5. Evaluation of the sensing efficiency 
it can increase in presence of Mobile PUs
This is the first work in literature that addresses the above issues !!

## Slide 15: Network Models
15
  PU Mobility Model (Assumption 1):
  * Memoryless mobility pattern constituted by a sequence of movement periods
  * During each period, a PU does not change its direction and its velocity
      Assumption 1 is assumed as general mobility model.
Notes: 15

## Slide 16: Network Models
16
  PU Traffic Model:
  Two state birth-death process with death rate α and birth rate β
  ON (Busy) State: PU  active with probability Pon= β/(α+β)
  OFF (Idle) State: PU  inactive with probability Poff= α/(α+β)
* CR User Network Model
  CR users static, uniformly distributed in the network region A,
  assumed either as a line or as a square.
Notes: 16

## Slide 17: Mobility-Aware Sensing Design: Overview
First Part of the paper:
  Characterization of the PU inter-arrival time for a general mobility model
Second Part of the paper:
  Derivation of the optimal sensing time parameters (sensing time and
  transmission time), by exploiting the results of the first part
Third Part of the paper:
  Specialization of the previously derived results for RWM.
Notes: 17

## Slide 18: Mobility-Aware Sensing Design: Some Definitions
18
PU Protection Range R
  To avoid any interference on PUs,
  CR users detect active PUs within a range R, called PU Protection Range
  (determined by PU transmission range and by CR interference range)
Maximum Interference Prob Pint
  Pint  max. value of the interference prob. that a PU can tolerate
Event I: CR user is inside the PU protection range
Event O: CR user is out of the PU protection range

## Slide 19: Mobility-Aware Sensing Design: Some Definitions
19
CR Interference Region:
  C(xCR) is a disk of radius R (PU protection range) around the CR user location xCR.
  Any CR user is inside the PU protection range R (Event I occurs),
  if the PU is placed within the CR interference region C(xCR),
  i.e., if the Euclidean distance between the CR user and the PU is not greater than R.
  Event I occurs: Event O occurs:
R
xCR
PU
R
xCR
PU
C(xCR)
C(xCR)

## Slide 20: Mobility-Aware Sensing Design: Some Definitions
20
MOVEMENT LENGTH L:
  RV L  Euclidean distance covered by a PU during a movement period
MOVEMENT DURATION D:
  RV D  time spent by a PU to complete a movement period
L=li
xPU(tα)
xPU(tβ)
tα
tβ
time
D=di=tβ-tα
Notes: In the figure, a realization of the random variable L , i.e., L=li, is shown along with a realization of the random variable D, i.e., D=di. Specifically, xPU(tα) and xPU(tβ) denote the PU locations at the time instant tα and tβ, respectively. Hence the time the PU spends to complete the movement is D=dii= tβ – tα, and the Euclidean distance covered by the PU is L=li.

## Slide 21: Mobility-Aware Sensing Design: Some Definitions
21
Out Time Θ:
  Time interval a PU (starting from its steady-state spatial distribution) spends out of the interference region of an arbitrary CR user:
|||| denotes the Euclidean distance
∧ denotes the logical operator “and”.
PU Arrival
t
Time
t1
PU Arrival
PU Departure
Θ
Notes: Infimum (partially ordered sets) (greatest lower bound)
The out time is the difference between the first time (t) the PU re-enters in the CR interference region and the last time (t1) the PU was in the CR interference region, with t1<t
t-1 denotes the left limit, i.e, lim_(epsilon -->0 ) (t1-epsilon), hence with the notation XPU(t1^-) we denote the evaluation of the PU location XPU(.) in a time instant that goes to t1 from the left side: XPU(t1^-)=lim_(epsilon ->0) XPU(t1-epsilon)
t1^+ denotes the right limit, i.e., lim_(epsilon -->0 ) (t1+epsilon), hence with the notation XPU (t1^+) we denote the evaluation of the PU location XPU(.) in a time instant that goes to t1 from the right side: XPU (t1^+)=lim_(epsilon ->0) XPU(t1+epsilon).
Hence, with the theta formula, we are saying that the out time is the time interval the PU spends out of the CR interference region such that at time t1^- the PU is still inside the CR interference region and at time t1^+ the PU is out

## Slide 22: Mobility-Aware Sensing Design: Some Definitions
22
Out Time Θ: Time interval a PU spends out of the CR interference region
R
XCR
XPU(t1-)
C(xCR)
R
XCR
XPU(t1+)
R
XCR
XPU(t)
PU Arrival
t
time
t1
PU Arrival
PU Departure
Θ
Notes: - At time t1^- the PU is still inside the CR interference region C(XCR) (the Euclidean distance between the PU location and the CR location is smaller than R),
At time t1^+ the PU is out of the CR interference region
Time t is the first (inf_{t >t1 }) time instant in which the PU re-enters in the CR interference region (the Euclidean distance between the PU location and the CR location is smaller than R)

## Slide 23: Out Time: Numerical Example
23
Out Time Θ:
  Assume:
    R=30m, t1= 3 sec., t= 7 sec. Θ = (7-3) sec= 4 sec.
R
XCR
XPU(t1-)
C(xCR)
R
XCR
R
XCR
XPU(t)
XPU(t1+)
Notes: - At time t1^-= 3-, the PU is still inside the CR interference region C(XCR) (the Euclidean distance between the PU location and the CR location is smaller than R=30m),
At time t1^+ the PU is out of the CR interference region (the Euclidean distance between the PU location and the CR location is greater than R=30m),
Time t is the first (inf_{t >t1 }) time instant in which the PU re-enters in the CR interference region (the Euclidean distance between the PU location and the CR location is smaller than R=30m)
With these values, the out time, i.e., the difference between the first time (t) the PU re-enters in the CR interference region and the last time (t1) the PU was in the CR interference region, with t1<t, is equal to 4sec.

## Slide 24: Mobility-Aware Sensing Design: Some Definitions
24
Sojourn Time S:
  Time interval a PU (starting from its steady-state spatial distribution) spends inside a CR interference region:
|||| denotes the Euclidean distance
∧ denotes the logical operator “and”.
PU Arrival
t
Time
t0
PU Arrival
PU Departure
S
Notes: Hence, with the S formula, we are saying that the sojourn time is the time interval the PU spends inside the CR interference region such that at time t0^- the PU is out of the CR interference region and at time t0^+ the PU is inside. To evaluate the sojourn time, we need to consider the greatest t (sup_(t >t0) ) such that at time t the PU is still inside the CR interference region.

## Slide 25: Mobility-Aware Sensing Design: Some Definitions
25
Sojourn Time S: Time interval a PU spends inside a CR interference region
R
XCR
XPU(t0+)
C(xCR)
R
XCR
XPU(t0-)
R
XCR
XPU(t)
XPU(t0+)
PU Arrival
t
Time
t0
PU Arrival
PU Departure
S
Notes: - At time t0^- the PU is out of the CR interference region C(XCR) (the Euclidean distance between the PU location and the CR location is greater than R),
At time t0^+ the PU is inside the CR interference region
Time t is the last (sup_{t >t0 }) time instant in which the PU is inside the CR interference region (the Euclidean distance between the PU location and the CR location is smaller than R)

## Slide 26: Sojourn Time: Numerical Example
26
Sojourn Time S:
  Assume:
    R=30m, t0= 10sec, t= 11sec S = (11-10) sec = 1sec.
R
XCR
XPU(t0+)
C(xCR)
R
XCR
XPU(t0-)
R
XCR
XPU(t)
XPU(t0+)
Notes: - At time t0^-=10- sec the PU is out of the CR interference region C(XCR) (the Euclidean distance between the PU location and the CR location is greater than R=30),
At time t0^+= 10+ the PU is inside the CR interference region
Time t=11 is the last (sup_{t >t0 }) time instant in which the PU is inside the CR interference region (the Euclidean distance between the PU location and the CR location is smaller than R=30m)
With these values, the sojourn time, i.e., the difference between the last time (t) the PU is in the CR interference region and the first time (t0) the PU was in the CR interference region, with t0<t, is equal to 1sec.

## Slide 27: Mobility-Aware Sensing Design: Some Definitions
27
Inter-Arrival Time T:
  Time interval between two consecutive arrivals of the PU in the interference region of a CR user.
  Inter-arrival time T is equal to the sum of the sojourn time and of the out time:
PU Arrival
t
Time
t0
PU Arrival
S
Θ
T

## Slide 28: Inter-Arrival Time: Numerical Example
28
Inter-Arrival Time T:
  From examples on Slides 23 and 26:
  S = 1sec and Θ = 4sec T =(1+4)sec = 5sec
PU Arrival
t
Time
t0
PU Arrival
S=1sec
Θ=4sec
T=5sec

## Slide 29: Mobility-Aware Sensing Design: Overview
First Part of the paper:
-Characterization of the PU inter-arrival time for a general mobility model
Second Part of the paper:
  Derivation of the optimal sensing time parameters (sensing time and
  transmission time), by exploiting the results of the first part
Third Part of the paper:
  Specialization of the previously derived results for the RWM
Notes: 29

## Slide 30: Primary-User Inter-Arrival Process: Average Value of the Inter-Arrival Time
30
  Theorem 1: Average inter-arrival time of a PU roaming within a network region A according to a general mobility model is:
with:
  * P(I) is the prob of event I.; i.e., % of time that a CR user is located within PU protection range R
* the average out time is equal to
* pdf of the CR user spatial distribution
* pdf of the PU steady-state spatial distribution, i.e., the PU spatial distribution after the
transition
* fL(l) pdf of the RV L (Defined in slide 20)
* average value of the RV D (Defined in slide 20)
Notes: Through slides 30-32, we describe the First Part of the paper, i.e., we characterize the PU inter-arrival time T (defined in slide 27) for a general mobility model, by deriving closed-form expressions for both its average value E[T](Theorem 1, slide 30) and its Cumulative Distribution Function (CDF) (Theorem 2, slide 33). These results will be used to set the optimal mobility-aware sensing time parameters, i.e., the sensing time and the transmission time (second part of the paper, slide 35-51).
A general mobility model is any mobility model satisfying Assumption 1 (slide 15). RWM and RWMP are examples of mobility models satisfying Assumption 1 (slide 15). In the third part of the paper we specialize the results derived with reference to a general mobility model for the RWM and the RWPM.

## Slide 31: Primary-User Inter-Arrival Process
31
Average value of the Inter-Arrival Time
  holds for every mobility model satisfying Assumption 1 (Slide 15).
  Depends on three factors:
    PU mobility model, through the PU steady-state spatial distribution
    fL(l), and
    CR spatial distribution
    Prob P(I) of an arbitrary CR user being inside the PU protection range.

## Slide 32: Average Value of the Inter-Arrival Time: Numerical Example
32
  Theorem 1:
    Assume: P(I) = 0.03 and
With this setting, the average time between two consecutive arrivals of a PU inside the CR interference
region is roughly 10.3 sec. This means a CR user waits in average 10.3 sec before to meet again the PU.
Notes: When we will specialize the results for the RWM and the RWPM (third part of this presentation), we will understand how the mobile PU parameters, e.g., the average PU velocity, the PU protection range etc., affect the calculation of these quantities (Theta, T etc.)(see examples reported in the third part of this presentation)

## Slide 33: Primary-User Inter-Arrival Process: Cumulative Distribution Function (CDF) of the Inter-Arrival Time
33
  Theorem 2: CDF of the inter-arrival time of a PU roaming within a network region A according to a general mobility model is bounded by:
where is the average value of the RV D and Pg(xCR) is the prob that a mobile PU meets the CR user (with location xCR) during a PU movement and given by:
Notes: Theorem 2 is saying that the probability that the inter-arrival time assumes values smaller than t, i.e., its CDF, is bounded by an exponential low dominated by the parameter Pg(xCR).
Pg(xCR) represents the probability that a mobile PU meets the CR user (whose location is xCR) during a PU movement.
It is composed by two integral since:
the first integral (int_C(XCR, l )) represents the probability that a mobile PU meets the CR user (whose location is XCR) during a PU movement of length L=li (the r.v. L is defined in slide 20)
the second integral (int_L) is necessary to remove the conditioning with respect to L=li.

## Slide 34: CDF of the Inter-Arrival Time: Numerical Example
34
  Theorem 2:
Consider a squared network region A=[0,a]x[0,a] and assume Pg(xCR) independent from the CR user location with
since , it results:

## Slide 35: Mobility-Aware Sensing Design: Overview
First Part of the paper:
  Characterization of the PU inter-arrival time for a general mobility model
Second Part of the paper:
  Derivation of the optimal sensing time parameters (sensing time and
  transmission time), by exploiting the results of the first part
Third Part of the paper:
  Specialization of the previously derived results for the RWM
Notes: 35

## Slide 36: Optimal Mobility Aware Sensing Parameters
36
Find Optimal Mobility Aware Sensing Parameters
(Sensing Time Ts and Transmission Time TTX)
STEPS:
  Optimal Mobility-Aware Transmission Time
  Optimal Mobility-Aware Sensing Time Threshold
  Mobility-Aware Sensing Time
Notes: 36
  Here by exploring the characterization of the inter-arrival time (derived in the previous slides), we address the proper selection of the sensing parameters. This is crucial for the performance of CR networks since the sensing time and the transmission time influence both the spectrum efficiency and interference avoidance.

## Slide 37: Optimal Mobility-Aware Transmission Time
37
Definition: is the transmission time that:
  * allows a CR user to respect the PU interference constraint
  * maximizes the sensing efficiency for a given value of the sensing time.
Notes: 37

## Slide 38: Optimal Mobility-Aware Transmission Time
38
Theorem 3: Consider a PU roaming in a network region A according to a general mobility model, then
  where:
  CDF of the PU inter-arrival time (Theorem 2)
  * Pint maximum interference probability
  Pon PU on-state probability
Notes: 38
A general mobility model is any mobility model satisfying Assumption 1 (slide 15).

## Slide 39: Explanation
  .
39
During two PU arrival events, a CR can interfere an active PU during TTx
  TTx cannot exceed the maximum interference time an active PU can tolerate between two arrival events, i.e.:
Optimal transmission time is the
maximum TTx satisfying this equation
Notes: When the inter-arrival time (temporal distance between two consecutive arrivals of the PU in the CR interference region) is lower then the transmission time, then the CR user can interferes with the active PU, since the PU arrives during the transmission time.
Hence, we want that the probability of a PU I) being active (P_on) and ii) arriving during the CU transmission time ( P(T<= T_Tx) is lower then the PU interference constraint (P_int).

## Slide 40: Optimal Mobility-Aware Transmission Time: Numerical Example
40
Theorem 3:
Given: Pint/Pon= 0.45 and reported in Figure
A CR User can transmits for 2 sec,
by satisfying the PU interference
constraint
Notes: 40

## Slide 41: Optimal Mobility-Aware Sensing Time Threshold
Definition: Optimal sensing time threshold is the maximum value of the sensing time assuring that:
    the sensing accuracy does not increase by observing the band for times
    longer than , regardless of the adopted sensing technique.
41
Sensing Time
Ψsopt
Sensing Accuracy
Notes: 41

## Slide 42: Optimal Mobility-Aware Sensing Time Threshold
42
Theorem 4: The optimal sensing time threshold is equal to the average sojourn time of a mobile PU inside the CR interference region:
  where:
  and given in Theorem 1
  P(I): prob. of a CR user being inside the PU protection range,
  i.e., % of time that a CR user is located within R.
Notes: 42
Theorem 4 is saying that observing the band for a time longer than the average sojourn time does not increase the sensing accuracy.
This agrees with the intuition: if the event O occurs, i.e., if the PU is not in the CR interference region, the CR user can use the band without interfering the PU, hence it is useless to waste time by sensing a free band.
Slides 45-47 provides a formal proof for Theorem 4.

## Slide 43: Optimal Mobility-Aware Sensing Time Threshold: Graphical Representation
43
Theorem 4: is equal to the average sojourn time
Sensing time
Sensing Accuracy
PU Arrival
t
time
t0
PU Arrival
PU Departure
S
=
Notes: 43

## Slide 44: Optimal Mobility-Aware Sensing Time Threshold: Numerical Example
44
Theorem 4:
Utilize the same values of the prev. example:
P(I)=0.03,
The maximum value of the sensing time, i.e. the sensing time threshold, , is equal to 0.31 sec.
Notes: 44

## Slide 45: Explanation
Hypothesis Test for CR users under Event I:
  CR user can sense the PU transmissions
Hypothesis Test for CR users under Event O:
CR user cannot sense the PU transmissions
45
R
PU
CR
R
PU
CR
Ho: no PU signal, H1: PU signal
Notes: 45

## Slide 46: Explanation
Hence the Detection and the False Alarm Probabilities:
    Y and γ denote the decision variables and the threshold of the generic adopted sensing technique, respectively.
46
If the event O occurs, the CR user cannot sense the PU
Notes: 46

## Slide 47: Explanation
Consequently
  Pd affected only by the event I
  Pf affected by both the events I and O with
From Pd and Pf it follows that observing the spectrum for a time greater
than the average sojourn time S has two effects:
  Pd does not improve
  Pf can increase
agrees with the intuition: if the event O occurs, the CR user can use the spectrum without interfering the PU
  it is useless to waste time by sensing a free spectrum.
47
According to the definition of ,
Notes: 47

## Slide 48: Mobility-Aware Sensing Time
48
Corollary 1: Consider a PU roaming within a network region A according to a general mobility model.
The mobility-aware sensing time Ts must be set:
    Direct consequence of Theorem 4
Notes: 48
Corollary 1 is saying that the sensing time cannot exceed the average sojourn time, since we have proved (Theorem 4, slide 42) that observing the band for a time longer than the average sojourn time can decrease the sensing accuracy

## Slide 49: Mobility-Aware Sensing Time: Numerical Example
49
Corollary 1:
From the example:
A CR user senses the spectrum for a time not longer than 0.31 sec.
Notes: 49

## Slide 50: Mobility-Aware Sensing Time
50
Insight: The amount ν(Pd;Pf) of the average sojourn time used for sensing depends on:
  required detection accuracy (Pd; Pf) &
  adopted sensing technique.
  Hence
  ν(Pd;Pf) accounts for the targeted detection accuracy and the adopted sensing technique characteristics.
Notes: 50
This provides a practical rule for setting Ts according to the mobile PU dynamics
T^ is the average inter-arrival time of a PU roaming within a network region A derive din Theorem 1 (slide 30)
P(I) denotes the percentage of time that the CR user is located within the PU region

## Slide 51: Mobility-Aware Sensing Time
51
Insight:
  If then Ts 0
    if the CR is never in the PU protection range, it is useless to sense the spectrum
  If i.e., if CR is always in the PU protection range,
  Ts must be set according to the static scenario rules or
  duality if the PU is always in the CR interference region
Notes: 51

## Slide 52: Mobility-Aware Sensing Design: Overview
First Part of the paper:
  Characterization of the PU inter-arrival time for a general mobility model
Second Part of the paper:
  Derivation of the optimal sensing time parameters (sensing time and
  transmission time), by exploiting the results of the first part
Third Part of the paper:
  Specialization of the previously derived results for RWM
Notes: 52
RWM and RWMP are examples of mobility models satisfying Assumption 1 (slide 15). In the third part of the paper we specialize the derived results for the RWM and the RWPM.

## Slide 53: Random Walk Mobility Model (RWM)
53
A PU chooses uniformly at random both a direction and a velocity in the intervals [0; 2π] and [vmin; vmax] m/s
Each movement occurs in a constant time
When the edge of the network region A is reached, the PU is bounced back to the region A.
Uniform steady-state spatial distribution regardless of the average PU speed

## Slide 54: Random Walk Mobility Model (RWM): Graphical Representation
54
xPU(tα)
xPU(tβ)
xPU(tγ)
v1T
v2T
ω1
ω2
Network Region A
At time tα , the PU in position xPU(tα)
randomly selects a direction ω1 and a
velocity v1
Then PU moves for a constant time T,
reaching the position xPU(tβ) at time tβ
Here, PU selects a new direction ω2 and
speed v2 according to the same rule
Since during this movement, PU reaches
the edge of A & is bounced back to
the region until reaching the position
xPU(tγ) at time tγ

## Slide 55: Primary-User Inter-Arrival Process for RWM
55
Theorem 1 for RWM: The average inter-arrival time of a PU roaming within a network region A according to the RWM is:
Θ is the average out time (average time interval a PU spends out of interference region of a CR user)
vRWM is the average PU velocity
PRWM(I) is the prob of event I (% of time a CR user is located within R)
for one-dimensional and bi-dimensional network regions, respectively
One-dimensional Network region
Bi-dimensional Network region
Notes: This slide provides the specialization of Theorem 1 in slide 30 for the RWM
The expressions of P1D-RWM (I) and P2D-RWM (I) are not reported since are complicate but these expression depend only on the normalized protection radius R/a. A reader interested in their expressions can find them in the paper

## Slide 56: Primary-User Inter-Arrival Process for RWM
56
depends on three factors:
  Average PU velocity
  Normalized protection radius R/a
  Size of the network region A

## Slide 57: Average Value of the RWM Inter-Arrival Time: Numerical Example
57
Theorem 1 for RWM:
Assume:
A squared network region A=[0,a]x[0,a]
R/a=0.01
i.e, CR user waits on the average roughly 250 sec
before to meet again a PU that is moving according to the RWM.

## Slide 58: Primary-User Inter-Arrival Process for RWM
58
Theorem 2 for RWM:
The CDF of the inter-arrival time of a PU roaming within a network region A according to the RWM is bounded by an exponential distribution:
One-dimensional Network region
Bi-dimensional Network region
Notes: This slide provides the specialization of Theorem 2 in slide 33 for the RWM.
Here we are saying that the probability that the inter-arrival time assumes values smaller than t, i.e., its CDF, is bounded by an exponential distribution of parameter ΩRWM

## Slide 59: CDF of the Inter-Arrival Time for the RWM: Numerical Example
59
Theorem 2 for RWM:
Assume:
A squared network region A=[0,a]x[0,a]
R/a=0.01

## Slide 60: Optimal Mobility-Aware Transmission Time for RWM
60
According to Theorem 3, the optimal mobility-aware transmission time for RWM is:
where is given by Theorem 2 for RWM:
By combining these two results, the following bound is derived:
where θ is the average out time for the RWM.
According to this result, a CR user can transmit for a longer time than the product between the average out-time and
Notes: Theorem 3 in slide 38 provides the rule for setting the optimal mobility-aware transmission time.
Here we are saying that by exploiting the bound derived for the RWM CDF we are able to set the optimal mobility-aware transmission time for this mobility model

## Slide 61: Optimal Mobility-Aware Transmission Time for RWM
  The lower bound provides a practical rule for setting TTX in mobile
  scenarios, in fact
    TTX shorter than the derived bound causes sensing inefficiency
    TTX longer than the derived bound can violate the PU interference constraint.
61

## Slide 62: Optimal Mobility-Aware Transmission Time for RWM: Numerical Example
Assume:
  A=[0,a]x[0,a]
  R/a=0.005
  Pint=10-2
  Pon = 0.2
62
A CR user can transmit for 10.26 sec
Notes: Here we considered a different simulation setting (e.g. R/a=0.005 instead of 0.01) to show to the students how the different mobile parameters affect the sensing time parameters

## Slide 63: Mobility-Aware Sensing Time for RWM
63
According to Corollary 1 & the related insight, the mobility-aware sensing time for the RWM is
  where is given by Theorem 1 for RWM:
By combining these two results, the mobility-aware sensing time for the RWM is given by:
One-dimensional Network region
Bi-dimensional Network region
Notes: 63
Corollary 1 in slide 48 provides the rule for setting the optimal mobility-aware sensing time.
Here we are saying that by exploiting the average sojourn time derived for the RWM we are able to set the optimal mobility-aware sensing time for this mobility model
P1D-RWM (I) and P2D-RWM (I) (slide 55):
  the probabilities of the event I (CR inside PU protection range) for one-dimensional and bi-dimensional network region
  their expressions depend only on the normalized protection radius R/a
  Their expressions are not reported since are complicate but a reader interested in their expressions can find them in the paper

## Slide 64: Mobility-Aware Sensing Time for RWM: Numerical Example
64
Continue the Example:
A=[0,a]x[0,a]
R/a=0.005
ν(Pd, Pf) =1
Since PU is very fast and at the same time has a small protection
range compared to the network region A, a CR user must sense the
channel for just 0.016 sec.
It can transmit for 10.26 sec.
High sensing efficiency by respectingat the same time the PU interference constraint
Notes: 64

## Slide 65: Mobility-Aware Sensing Time for RWM: Some Considerations
65
Ts depends on:
  normalized PU protection range R/a
  extension of the network area A
  average PU velocity
  sensing accuracy ν(Pd, Pf)
Notes: 65

## Slide 66: Mobility-Aware Sensing Efficiency
66
Definition: The mobility-aware sensing efficiency is the ratio of the optimal transmission time over the entire sensing period
By using the derived results, a lower bound of the sensing efficiency is evaluated.
Notes: 66
In slides 12-13 (Contributions) we have underlined that the sensing accuracy can increase in presence of Mobile PUs.
In this slide we show this statement.

## Slide 67: Mobility-Aware Sensing Efficiency
67
ηmob depends on 3 factors:
  PU Interference Constraint Pint
  PU Mobility Model
  PU Traffic
ηmob reflects the dynamic nature of
  PU topology through P(I)
  PU traffic through Pon.
Given Ts, Pint and Pon, ηmob increases when
increases
  CR user spends more time out of the PU range and thus it can use the spectrum for a longer time with the same Pint
Given Ts, Pint and if
  CR user can transmit in an arbitrarily long time interval
Notes: 67
To derive this formula, we have substituted in the definition of the sensing efficiency the derived bound for the optimal transmission time

## Slide 68: Results: Optimal Mobility-Aware Transmission Time
When R/a increases, TTx decreases
    CR spends more time in the PU range
When Pon increases, TTx decreases
    PU traffic dynamics increase
    TTx is set according to the lower bounds, Pint= 10-2, vmin/a=0.1, vmax/a= 0.9
Theoretical results match well the simulation results

## Slide 69: Results: Optimal Mobility-Aware Transmission Time
The results confirm the benefits of setting TTx according to our results:
    the average interference levels on the PU for
    RWM are 910-3 < Pint and 610-3 < Pint
    Instantaneous Interference Level on the PU transmissions,
    Pint= 10-2 (represented in the figures with the red lines), Pon= 1/3

## Slide 70: Results: Optimal Mobility-aware Sensing Time Threshold
    False-alarm probabilities versus Ts,
    SNR= -5 dB, Energy Detector, Pd=0.999
The results validate the analysis:
  for Ts longer than the average sojourn time S, Pf increases
  Threshold behavior in the sensing accuracy

## Slide 71: Results: Mobility-Aware Sensing Time
    Ts is set according to the analytical results for ν(Pd,Pf)=1
theoretical results match well the simulation results
when R/a increases, Ts increases
    CR probability of being inside the PU range increases
when v/a increases, Ts decreases
    CR spends more time out of the PU range

## Slide 72: Conclusions
72
Mobile PU dynamics force researchers to revise the current
design of the sensing functionality for jointly
  maximizing the sensing efficiency
  satisfying the PU interference constraint
Sensing Time and Transmission Time Optimization
  Two fundamental questions are answered:
    How often must the sensing be performed in presence of PU mobility?
    How long must a spectrum band be sensed to reliably detect mobile PUs?
  A threshold behavior in the sensing accuracy as a function of the sensing time

## Slide 73: Conclusions
73
The developed optimal mobility-aware sensing design
exhibits a very attractive feature:
  It does not depend on the instantaneous values of the PU mobility
  pattern but only on the average statistics such as average PU
  sojourn time and the average PU out time