## Slide 1
CHAPTER 9.
COMMON CONTROL CHANNELS

## Slide 2: Outline
Introduction to Common Control Channel (CCC)
  CCC Classification
CCC Design Challenges
CCC Solutions
  CCC Solutions in CR MAC Protocols
  Sequence-based CCC Solutions
  Group-based CCC Solutions
  Underlay CCC Solutions
  Our CCC Solutions
Research Challenges

## Slide 3: Common Control Channel (CCC)
Definition
  A CCC in a CR network is defined as a medium temporarily or permanently allocated in a portion of licensed or unlicensed spectrum commonly available to two or more CR users for control message exchange
B. F. Lo, “A survey of common control channel design in cognitive radio networks,” Physical Communication (Elsevier) Journal, vol. 4, no. 1, March 2011.

## Slide 4: Why CCC?
CCC facilitates CR network operations
  Physical (PHY) layer
    Exchange spectrum sensing information for CR user cooperation
  Link/MAC layer
    Notify PU activity and spectrum opportunities
    Signal beacons or broadcast Hello packets for neighbor discovery
    Channel access negotiation
    Transmitter–receiver (RTS-CTS) handshake
  Network layer
    Broadcast route requests
    Notify topology updates

## Slide 5: CCC Classification
Overlay vs. Underlay
  Overlay
    CCC allocated to the spectrum temporarily or permanently not used by PUs
    Must vacate CCC if a PU occupies CCC
    CCC is subject to PU activity
  Underlay
    CCC can be allocated to the spectrum currently used by PUs
    Control transmissions are spread over a large bandwidth in the spectrum and appear to PU as noise
    CCC is not affected by PU activity

## Slide 6
In-band vs. Out-of-band
  Out-of-band CCC (Dedicated CCC)
    A predefined channel dedicated to CR users for control message exchange
    Channel exclusively used for control purposes
      Reserved by regulatory authorities (e.g. FCC)
      Predefined or statically allocated in unlicensed or licensed band
      Always available to CR users locally or globally
     Not affected by PU activity (usually assumed in CR MACs)
6
CCC Classification: Overlay
Notes: 6

## Slide 7: CCC Classification: Overlay
In-band vs. Out-of-band
  In-band CCC
    Channels are dynamically allocated to and temporarily shared among CR users for control message exchange
    CCC shares the same channel used for data
      Dedicated CCC not always feasible in some applications
      Allocated dynamically and locally for a temporary duration
    Major design choices: group-based or sequence-based CCC
     Subject to PU activity anytime

## Slide 8
Major CCC Design Solutions
  Sequence-based CCC (overlay, in-band)
  Group-based CCC (overlay, in-band)
  Dedicated CCC (overlay, out-of-band)
  Ultra Wideband (UWB) CCC (underlay)
Different design challenges encountered in each type of CCC solutions
CCC Classification: Major Solutions

## Slide 9: CCC Design Challenges (CCC Problems)
Control Channel Saturation
  Performance degrades as a large number of CR users compete for CCC access
Robustness to PU Activity
  CCC may not be available all the time due to PU activity
CCC Coverage
  Limited CCC coverage creates control signaling overhead
Control Channel Security
  Vulnerability to security attacks (e.g., jamming)
9
Notes: 9

## Slide 10: CCC Problem: Control Channel Saturation
Problem Definition
  Collision rate significantly increases as a large number of nodes compete for CCC access resulting in considerably reduced throughput
10
L. Ma, X. Han, and C.-C. Shen, “Dynamic Open Spectrum Sharing MAC Protocol for Wireless Ad Hoc Networks,” Proc. of IEEE DySPAN 2005, Nov. 2005
Notes: 10

## Slide 11: Possible Solutions: Control Channel Saturation
Limit control traffic
Adjust CCC bandwidth
  SRAC
Migrate CCC to a better channel
  SOCC
Balance control traffic over several channels
  SYN-MAC, Sequence-based Rendezvous
11
Notes: 11

## Slide 12: CCC Problem: Robustness to PU Activity
Problem Definition
  CR users cannot be guaranteed a new CCC when they must immediately vacate CCC upon a PU arrives !
    CCC may not be available all the time due to PU activity
12
I. F. Akyildiz, W.-Y. Lee, and K. R. Chowdhury,
“CRAHN: Cognitive Radio Ad Hoc Networks,”
Ad Hoc Networks (Elsevier) Journal, 2009
Notes: 12

## Slide 13: Possible Solutions: Robustness to PU Activity
Dynamic CCC allocation
  Dynamic CCC allocation based on spectrum opportunity and PU activity
    C-MAC, SI-based CCC, ERCC
Efficient CCC Recovery
  Recover CCC efficiently and maintain CR network topology
    ERCC
13
Notes: 13

## Slide 14: CCC Problem: CCC Coverage
Problem Definition
  Dynamic PU activity and connectivity make a fixed CCC for all CR users infeasible
    In-band CCC coverage usually limited to a local area
    High communication overhead for large number of CCCs
14
I. F. Akyildiz, W.-Y. Lee, and K. R. Chowdhury,
“CRAHN: Cognitive Radio Ad Hoc Networks,”
Ad Hoc Networks (Elsevier) Journal, 2009
Notes: 14

## Slide 15: Possible Solutions: CCC Coverage
Clustering
  Use clustering structure with topology management
    SOCC
Neighbor Coordination
  Combine neighbor’s information locally for CCC allocation
    SI–based CCC, ERCC
15
Notes: 15

## Slide 16: CCC Problem: Jamming Attack
Problem Definition
  Control traffic on CCC maliciously interfered or blocked by adversaries
16
L. Ma, C.-C. Shen, and B. Ryu,
“Single-Radio Adaptive Channel Algorithm for Spectrum Agile Wireless Ad Hoc Networks,”
IEEE DySPAN 2007, Apr. 2007
Notes: 16

## Slide 17: Possible Solutions: Jamming Attack
Possible Solutions
  Anti-jamming by dynamic CCC allocation
    Use different in-band CCCs for outgoing and incoming control traffic in response to jamming (SRAC: cross channel communication)
    Distribute controls over several channels to avoid single point of failure (Sequence-based rendezvous, quorum-based CCC: frequency hopping)
  Anti-jamming by CCC key distribution
    Control messages are repeatedly transmitted on multiple CCCs
    Any compromised nodes having only partial keys in the key space will not be able to jam all the CCCs
    Jamming-resilient key assignment can be polynomial-based or randomly distributed
17
B. F. Lo, “A survey of common control channel design in cognitive radio networks,” Physical Communication (Elsevier) Journal, vol. 4, no. 1, March 2011.
Notes: 17

## Slide 18: Overview of Solutions for CCC Problems
Solutions for CCC Problems |  |  | 
Control Channel Saturation | Robustness to PU Activity | CCC Coverage | CCC Security (Jamming)
SYN-MAC SRAC Sequence-based Rendezvous | OFDM-based CCC ERCC UWB CCC | C-MAC SOCC Swarm Intelligence-based CCC ERCC | SRAC Quorum-based CCC
18
Notes: 18

## Slide 19: CCC Solutions in CR MAC Protocols
CCC is an inseparable part of every CR MAC protocol
  Dedicated CCC approach
    Not affected by PU activity (generally assumed)
  In-band CCC approach
    CCC subject to PU activity anytime
    In spotlight
      Synchronized MAC (SYN-MAC)
      Single-Radio Adaptive Channel (SRAC) MAC
      C-MAC

## Slide 20: SYN-MAC
In-band CCC Solution
  CR users are synchronized to coordinate data transfer in dedicated slots for control message exchange
  One of the data channels is used as the CCC in each dedicated slot
Sequence-based CCC Solution
  Control radio switches to a channel based on hopping sequence
  Channel hopping is sequential (e.g. 1,2,3,4,5,1,2,3,4,5…)
  CCC is allocated in round-robin fashion
Y. R. Kondareddy, P. Agrawal, “Synchronized MAC Protocol For Multi-hop Cognitive Radio Networks”, IEEE Int. Conference on Communications (ICC), May 2008.

## Slide 21: SYN-MAC Main Idea
Time is divided into time slots
Each time slot is dedicated to a channel for control signal exchange
At the beginning of each time slot, CR users with control packets wait for a random backoff and start negotiation (similar to IEEE 802.11 DCF)
If negotiation is successful, data transmission can start
Data transfer
TIME
Ch1
Ch5
Ch4
Ch3
Ch2
Backoff
Control packets
Slot for
channel 1
Data transfer
PU activity
PU activity
Slot for
channel 2
Slot for
channel 3
Slot for
channel 4
Slot for
channel 5

## Slide 22: CCC in SYN-MAC
Each slot dedicated to a channel for all control exchanges
All nodes in the neighborhood listen to the in-band CCC in the given slot
Dedicated radio for in-band CCC
22
Data transfer
TIME
Ch1
Ch5
Ch4
Ch3
Ch2
Backoff
Control packets
Slot for
channel 1
Data transfer
PU activity
PU activity
Slot for
channel 2
Slot for
channel 3
Slot for
channel 4
Slot for
channel 5
No CCC in Slots 3 & 5 due to PU activity
CCC
CCC
CCC
Notes: 22

## Slide 23: CCC Solution: SYN-MAC
Advantage
  Alleviate control channel saturation problem
    Control traffic distributed over channels in time slots
Drawbacks
  Disrupted CCC coverage
    No CCC available when control slots occupied by PUs
  No guarantee on timely PU protection
    PU activity can only be reported in specific time slots
    Vacating channels for PUs may not be in a timely fashion
  Predictable hopping pattern exposes the security risk
23
Notes: 23

## Slide 24: Single Radio Adaptive Channel (SRAC) MAC
Overview
  Dynamic Channelization for Control Channel Saturation
    Choose the usable channel BW dynamically based on the spectrum demand
  Cross-channel Communication for Jamming Attacks
    Uses different channels for transmitting and receiving when a channel is jammed
L. Ma, C.-C. Shen, and B. Ryu, “Single-Radio Adaptive Channel Algorithm for Spectrum Agile Wireless Ad Hoc Networks”, in Proc. of IEEE DySPAN, Apr. 2007.

## Slide 25: Dynamic Channelization for CCC Saturation
Definition:
Adaptive combination of spectrum bands based on the CR requirement
  Basic spectrum b is decided
  Actual spectrum is an odd multiple m·b of basic spectrum
  m is varied based on the spectrum demand
b
m·b
Actual Spectrum
Basic Spectrum

## Slide 26: Cross-Channel Communication for Jamming Attacks
26
3
1
0
2
4
3
1
0
2
4
3
1
0
2
4
Subnet 1
Subnet 2
Subnet 3
Subnet 1
Subnet 2
Subnet 3
Receive Channel = 0
Receive Channel = 4
Receive Channel = 1
Jamming
Jamming
Frequency
Jamming
Jamming
Notes: 26

## Slide 27: Cross-Channel Communication for Jamming Attacks
Different spectrums can be used for sending and receiving to avoid jamming and PU activity
If node 1 needs to change its receive channel, it sends a notification to its neighbors which reply with an ACK
CSMA channel access with random wait is assumed
Neighbor A (receive channel = 2)
ACK
Node 1
(initial receive channel = 1)
Neighbor B (receive channel = 1)
Not affected by Jamming
Jamming detected Change receive channel from 1 to 2
CSMA
CSMA
ACK
ACK
ACK
Random wait
Ch 2
Ch 2
Ch 1
Ch 2
(receive channel = 2)

## Slide 28: PU Activity Notification Problem
28
CSMA
PU detected and receive channel changed from 1 to 2
(receive channel = 1)
(receive channel = 2)
ACK
(receive channel = 1, not affected by PU)
CSMA
ACK
Node 1
Neighbor B does not know the change since no PU activity detected
(receive channel = 2)
Neighbor A
Neighbor B
PU Activity
Cannot notify Neighbor B due to PU activity on Ch 1
Ch 2
Ch 2
Cross-channel communication does not solve this problem
Notes: 28

## Slide 29: CCC Solution: SRAC
Advantages
  Alleviate saturation and jamming problems
    CCC bandwidth adaptively increased to avoid saturation
    Receive channel adapted for cross-channel communications in response to jamming
Drawbacks
  PU activity notification problem
  Limited CCC coverage
29
Notes: 29

## Slide 30: C-MAC
Main Idea
  Slotted behavior is enhanced by the use of superframes
  Rendezvous channel (RC) is exploited for neighbor discovery, load and scheduling information exchange
  Backup channels (BC) are also employed for coexistence
C. Cordeiro, K. Challapali, “C-MAC: A Cognitive MAC Protocol for MultiChannel Wireless Networks,” in Proc. of IEEE DySPAN, Nov. 2007.

## Slide 31: Important Concepts in C-MAC
RC (Rendezvous Channel)
  Used to coordinate nodes in different channels in order for the Beacon Periods (BP) not to overlap
  Multi-channel resource reservation
  Coordination for PU detection
BC (Backup Channel)
  Determined by out-of-band measurements
  Carried out by nodes when they are not engaged in communication or during quiet period

## Slide 32: C-MAC
Rendezvous Channels (RC)
  Primary CCC subject to PU activity
Backup Channels
  Backup CCC when PU returns to RC
32
BP (Beacon Period)
DTP (Data Transfer Period)
QP (Quiet Period)
BP
DTP
Superframe
BP
DTP
Superframe
BP
DTP
Superframe
QP
QP
QP
Channel A (RC)
Channel B
Channel C
Notes: 32

## Slide 33: CCC Solution: C-MAC
Advantages
  Increased robustness to PU activity
    Backup channel provides fast CCC recovery from PU activity on CCC
  Flexible CCC coverage
    RC can be distributed or extended for network-wide broadcast
Drawbacks
  Control overheads due to large volumes of beacon exchanges
  Single converging RC not always possible
  Inter-channel synchronization required for reliable RC
    Scheduling of non-overlapping beacon and quiet periods over a large number of channels is a nontrivial task
33
Notes: 33

## Slide 34: Overview of Major CCC Solutions
Major CCC Design Solutions |  |  | 
Sequence-based CCC | Group-based CCC | Dedicated CCC | Underlay CCC
SYN-MAC Sequence-based Rendezvous Quorum-based CCC | C-MAC SOC SI-based CCC ERCC | OFDM-based CCC | UWB CCC
34
Notes: 34

## Slide 35: Sequence-based CCC Solutions
CCCs are allocated according to a random or predetermined channel hopping sequence
Objective
  Diversify the control channel allocation over spectrum and time spaces in order to minimize the impact of PU activity and jamming attacks
In Spotlight
  Sequence-based Rendezvous
  Quorum-based CCC

## Slide 36: Sequence-based Rendezvous
Definition:
Rendezvous (Link rendezvous)
  Two or more CR users establish a link on a common channel
  In-band CCC solution
    All rendezvous channels used for both control and data
36
L. A. DaSilva and I. Guerreiro, “Sequence-based Rendezvous for Dynamic Spectrum Access,” in Proc. of IEEE DySPAN 2008, Oct. 2008
Notes: 36

## Slide 37: Sequence-based Rendezvous
Blind Rendezvous
  Random channel selection for scanning
    No bound on the time required for rendezvous
Sequenced-based Rendezvous
  Use non-orthogonal sequence for channel scanning
  Establish in-band CCCs on a link-by-link basis
  No dedicated CCC
  Robust to CCC saturation problems
37
L. A. DaSilva and I. Guerreiro, “Sequence-based Rendezvous for Dynamic Spectrum Access,” in Proc. of IEEE DySPAN 2008, Oct. 2008
Notes: 37

## Slide 38: Sequence Selections
Predefined Sequence
38
1
1
2
2
3
2
1
3
3
Sequence Change in Response to PU Activity
3
1
2
Selected permutations of N channels
Selected permutations of N channels
(N = 3)
1
1
2
2
3
2
1
3
3
3
1
2
1
1
3
1
3
3
3
1
new rendezvous sequence
if PU activity on channel 2
rendezvous sequence
if no PU activity
Remove all channels affected by PU activity
Notes: 38

## Slide 39: Sequence-based Rendezvous Example
39
1
1
2
2
3
2
1
3
1
1
2
2
3
2
1
3
Rendezvous on Channel 2
A
B
Predefined Sequence
  3 channels available
  {1, [1,2,3], 2, [2,1,3],
  3, [3,1,2]}
Channel Scanning
  Node A starts at t=0
  Node B starts at t=3
  Lag = 3
Rendezvous
  Complete at t=6 on Channel 2
  Time to Rendezvous = 3
0
1
2
3
4
5
3
4
5
3
3
1
2
3
lag
Time to Rendezvous
6
6
time
channel
CCC=Ch 2
Notes: 39

## Slide 40: CCC Solution: Sequence-based Rendezvous
  Advantage
    Robustness to CCC saturation problem
Drawbacks
  Limited adaptability to PU activity
    Not adaptable to new spectrum opportunities
    Responding to PU activity only by eliminating channels
  Long or unbounded rendezvous time
    No guarantee on bounded time to rendezvous if affected by PUs
  Very limited CCC Coverage
    Rendezvous only for point-to-point links with no broadcast support
40
Notes: 40

## Slide 41: Quorum-based Common Control Channel
Quorum-based Channel Hopping
  Control channels established by rendezvous using channel hopping sequences constructed from cyclic quorum systems
  Using sequences constructed from quorum systems increases the probability of rendezvous
    At least one channel common to two hopping sequences in each slot
  Rendezvous channels spread out in time and frequency
  Common hopping for data exchange after rendezvous
K. Bian, J.-M. J.-M. Park, and R. Chen, “Control Channel Establishment in Cognitive Radio Networks using Channel Hopping,” IEEE Journal on Selected Areas in Communications, vol. 29, no. 4, April 2011.

## Slide 42: Quorum System
Quorum System S under U
  A collection of non-empty subsets of U
    U = {0,…,n-1} is a finite universal set of n elements
  Satisfy the intersection property:
  Each p or q in S is called a quorum
Example
  S = {{0,1},{0,2},{1,2}} is a quorum system under U = {0,1,2}
  {0,1}, {0,2}, and {1,2} are quorums in S

## Slide 43: Example: Quorum-based Channel Hopping System
Each sequence consists of m frames, each frame consists of k slots
  Period of channel hopping (CH) sequence T = m • k = 9 (m = 3, k = 3)
Every pair of CH sequences rendezvous in m=3 different channels
  Set of rendezvous channels: R = {h0,…,hm-1} = {h0, h1, h2} = {0, 1, 2}
Construct a quorum system S = {q0, q1, q2} = {{0,1}, {0,2}, {1,2}} under Zk
  Sequences u, v, and w are constructed from quorums q0, q1, q2, respectively
0
0
0
0
h
0
0
h
1
1
h
h
1
1
1
1
h
h
h
h
h
2
2
2
2
2
2
u
v
w
slot index
0
1
2
3
4
5
6
7
8
1st Frame
2nd Frame
3rd Frame
CR user 1
CR user 2
CR user 3
Degree of overlapping = 3

## Slide 44: Example: Constructing a Sequence from a Quorum
Construct Sequence u from q0={0,1}
  u0=0: j=0, d=0, i=0 є q0, h0=0
  u1=0: j=0, d=0, i=1 є q0, h0=0
  u2=h: j=0, d=0, i=2
  u3=1: j=0, d=1, i=0 є q0, h1=1
  u4=1: j=0, d=1, i=1 є q0, h1=1
  u5=h: j=0, d=1, i=2
  u6=2: j=0, d=2, i=0 є q0, h2=2
  u7=2: j=0, d=2, i=1 є q0, h2=2
  u8=h: j=0, d=2, i=2
0
0
h
1
1
h
h
2
2
u
slot index
0
1
2
3
4
5
6
7
8
1st Frame
2nd Frame
3rd Frame
quorum index
channel index
slot index
in a frame
|S| = 3, m=3, k=3
random
random
random

## Slide 45: Example: Sequence Change Due to PU Activity
PU Activity
  Channels affected by PU activity are replaced by a channel randomly selected from the set of available channels
  The rest of the sequence remains unchanged
0
0
h
1
1
1
h
2
2
u
Before change
0
1
2
3
4
5
6
7
8
1st Frame
2nd Frame
3rd Frame
PU
PU
PU
0
0
h
0
2
h
h
2
2
u
After change
0
1
2
3
4
5
6
7
8
1st Frame
2nd Frame
3rd Frame
random
random
random

## Slide 46: Metrics of Channel Hopping Systems
Maximum Time-To-Rendezvous (MTTR)
  Maximum time for any pair of sequences to rendezvous
    Example: The MTTR is 3 in the example
0
0
0
0
h
0
0
h
1
1
h
h
1
1
1
1
h
h
h
h
h
2
2
2
2
2
2
u
v
w
slot index
0
1
2
3
4
5
6
7
8
1st Frame
2nd Frame
3rd Frame
CR user 1
CR user 2
CR user 3
MTTR = 3

## Slide 47: Metrics of Channel Hopping Systems
Load of Channel Hopping (CH) Systems
  The fraction of number of the times the busiest element used
    Busiest element: the (timeslot, channel)-pair included in the largest number of CH sequences
  Example: The load is 2/3 in the example
0
0
0
0
h
0
0
h
1
1
h
h
1
1
1
1
h
h
h
h
h
2
2
2
2
2
2
u
v
w
slot index
0
1
2
3
4
5
6
7
8
1st Frame
2nd Frame
3rd Frame
From q0 = {0,1}
Busiest element: (3,1)-pair included in 2 out of 3 CH sequences
Busiest element: (7,2)-pair
From q1 = {0,2}
From q2 = {1,2}

## Slide 48: Cyclic Quorum Systems (1)
Relaxed Cyclic (n,k)-difference Set D
  D = {a1,…,ak} is a relaxed cyclic (n,k)-difference set under Zn if for every d ≠ 0 (mod n) there exist ai and aj such that
  ai - aj = d (mod) n
Example
  D = {0,1,3} is a relaxed cyclic (7,3)-difference set under Z7
    1-0 ≡ 1 (mod) 7, 3-1 ≡ 2 (mod) 7, 3-0 ≡ 3 (mod) 7
    0-1 ≡ 6 (mod) 7, 1-3 ≡ 5 (mod) 7, 0-3 ≡ 4 (mod) 7

## Slide 49: Cyclic Quorum Systems (2)
Cyclic Quorum System
  A group of sets Bi = {a1+i,a2+i,…,ak+i} (mod) n, i = {0,1,…,n-1}, is a cyclic quorum system if and only if D = {a1,a2,…,ak} is a relaxed cyclic (n,k)-difference set
Example
  Given D = {0,1,3} under Z7, Bi = {0+i,1+i,3+i} mod 7, i = {0,1,…6}, is a cyclic quorum system
    B0 = {0,1,3}, B1 = {1,2,4}, B2 = {2,3,5}, B3 = {3,4,6},
    B4 = {4,5,0}, B5 = {5,6,1}, B6 = {6,0,2}

## Slide 50: Majority Cyclic Quorum Systems
Majority Cyclic Quorum System
  A cyclic quorum system S based on the difference set D that contains more than half of the elements in Zn
    D = {0,1,2} under Z4 (k = 3 > 4/2)
    S = {{0,1,2},{1,2,3},{2,3,0},{3,0,1}} is a majority cyclic quorum system
M-QCH System
  Constructed with a majority cyclic quorum system over Z3
  Optimal QCH design: minimize MTTR (k=3) while keeping the load < 1

## Slide 51: Minimal Cyclic Quorum Systems
Minimal Cyclic Quorum System
  A cyclic quorum system S based on the singer difference set D whose size k approximates the lower bound √n
    D = {1,2,4} under Z7 is a singer difference set (k = 3 ≈ √7 = 2.65).
    S = {{1,2,4}, {2,3,5},{3,4,6},{4,5,0},{5,6,1},{6,0,2},{0,1,3}} is a minimal cyclic quorum system
L-QCH System
  Constructed with a minimum cyclic quorum system over Zτ
  Near Optimal in terms of the load (close to theoretical minimum 1/√τ)
    τ is the maximum allowed MTTR

## Slide 52: Comparison of Channel Hopping Systems
 | Degree of overlapping | Load | MTTR | MCTTR
Blind Rendezvous | 0 | - | - | -
SSCH | 1 | 1/(N-1) | N+1 | -
M-QCH | N | 2/3 | 3 | 3N
L-QCH | N | ≥1/√τ | K | kN
Seq Rendezvous | 1 | 1/N | N(N+1) | -
A-QCH | 2 | ≈1/2 | ≥9 | -
A-MOCH | N | 1 | N2-N+1 | N2
Synchronous Quorum-based CCC
Asynchronous Quorum-based CCC
MCTTR: Maximum conditional TTR between 2 CH nodes when PU is present and at least one PU-free common channel is available

## Slide 53: Quorum-based Control Channels
Advantages
  Performance improvement over Sequence-based Rendezvous schemes
  Robust to control channel saturation and jamming problems
Disadvantages
  Subject to PU activity even with sequence adjustment
  No broadcast support and limited CCC coverage
  Long rendezvous time when the number of channel is large

## Slide 54: Group-based CCC Solutions
CCC is allocated to a channel commonly available to a group of CR users in proximity
Objective
  Form groups of CR users with common channels to increase CCC coverage and facilitate control message broadcast
In Spotlight
  Spectrum Opportunity-based Clustering (SOC)
  Swarm Intelligence-based CCC

## Slide 55: Spectrum Opportunity-based Control Channel
Spectrum Opportunity-based Clustering (SOC)
  Cluster-based Control Channel Solution
  Clustering design formulated as a maximum edge biclique graph problem
    Clusterhead is inherently selected during clustering
    CCC determined by the clusterhead
  CCC subject to PU activity
  Re-clustering is needed in response to PU activity
L. Lazos, S. Liu, and M. Krunz, “Spectrum Opportunity-Based Control Channel Assignment in Cognitive Radio Networks,” in Proc. of IEEE Secon’09, Jun. 2009.

## Slide 56: SOC Algorithm
Spectrum-Opportunity Clustering (SOC) Algorithm
  Step 1: Maximum edge biclique computation
    CR users individually compute their cluster memberships by solving the maximum edge biclique problem
  Step 2: Exchange and update cluster membership information
    CR users broadcast the computed information to neighbors
    Update cluster membership accordingly
    New cluster information is rebroadcasted
  Step 3: Finalize cluster membership
    CR users compute the final and unique cluster membership information
    Broadcast the final clusters and CCCs to ensure consistency with neighbors

## Slide 57: Step 1: Maximum Edge Biclique Computation
Clustering is formulated as a maximum edge biclique graph problem
From Graph Theory:
Bipartite Graph
  A graph G(V,E) is bipartite if V can be partitioned into two disjoint sets A and B (A U B = V) such that all edges in E connect vertices from A to B
Biclique
  A bipartite graph Q(X,Y) is a biclique if for each x є X and y є Y there exists an edge e є E between x and y

## Slide 58: Bipartite Graph Example
B
G
C
A
D
E
H
F
Bipartite Graph Constructed by CR user A (CRA)
B
C
D
G
H
A
1
5
2
3
4
6
AA = NbrA U A
BA = CA
10
  CA = {1,2,3,4,5,6,10}
  CB = {1,2,3,5,7}
  CC = {1,2,3,4,10}
  CD = {1,2,3,5,7}
  CE = {2,3,5,7}
  CF = {2,4,5,6,7,10}
  CG = {1,2,3,4,8}
  CH = {1,2,5,8}
Connectivity Graph and Channel Availability
Set of A and A’s neighbors
Set of available channels at A

## Slide 59: Maximum Edge Biclique Graph
Maximum Edge Biclique Graph Constructed by CRA
  j=1: XA={A}, YA=CA, PA[1]=7
  j=2: XA={A,C}, YA={1,2,3,4,10}, PA[2]=10
  j=3: XA={A,C,D}, YA={1,2,3}, PA[3]=9
  j=4: XA={A,C,D,B}, YA={1,2,3}, PA[4]=12
  j=5: XA={A,C,D,B,G}, YA={1,2,3}, PA[5]=15
  j=6: XA={A,C,D,B,G,H}, YA={1,2}, PA[6]=12
  j*=5: QA(XA,YA); XA={A,B,C,D,G}, YA={1,2,3}
10
B
C
D
G
A
1
2
3
XA
YA
QA(XA,YA)
 Maximizing the product of number of common channels and number of cluster members

## Slide 60: Step 2: Exchange and update information
CR user A receives updates from one-hop neighbors
  QA1: XA={A,B,C,D,G}, YA={1,2,3}
  QB1: XB={A,B,H}, YB={1,2,5}
  QC1: XC={A,B,C,D}, YC={1,2,3}
  QD1: XD={A,B,C,D,G}, YD={2,3}
  QG1: XG={A,D,G,H}, YG={1,2}
  QH1: XH={A,B,G,H}, YH={1,2}
   QG1 < QH1 < QB1 < QD1 < QC1 < QA1
   QG2 = QH2 = QB2 = QD2 = QC2 = QA2 = QA1
Qi < Qj if and only if
  |Xi| x |Yi| < |Xj| x |Yj|
  |Xi| x |Yi| = |Xj| x |Yj| and |Xi| < |Xj|
  |Xi| x |Yi| = |Xj| x |Yj|, |Xi| = |Xj|,
  |yi| = |yj|, i<j
60
B
G
C
A
D
E
H
F
  CA = {1,2,3,4,5,6,10}
  CB = {1,2,3,5,7}
  CC = {1,2,3,4,10}
  CD = {1,2,3,5,7}
  CE = {2,3,5,7}
  CF = {2,4,5,6,7,10}
  CG = {1,2,3,4,8}
  CH = {1,2,5,8}

## Slide 61: Step 3: Finalize Cluster Membership
Determine final cluster membership
  CR user A: QA3 = QA2
    XA3 = XA2, YA3 = YA2
  CR user B: QB3 = QB2
    XB2 = {A,B,C,D,G}
    B is included in bicliques of A,C,D,G
    XB3 = XB2, YB3 = YB2
  CR user H forms its own cluster
    XH2 = {A,B,C,D,G}
    H is not included in bicliques of A,B,C,D,G
    XH3 = {H}, YH3 = {1,2,5,8}
B
G
C
A
D
E
H
F
YE={2,5,7}
YH= {1,2,5,8}
YA= {1,2,3}
Finalized cluster membership

## Slide 62: CCC Solution: SOC
Problems
  Inter-cluster coordination problem
    Caused by heterogeneous channel availability between clusters
  Control channel migration problem
    Caused by PU activity or fading
Proposed solution: control channel hopping
  Control channel hops among the common channels within each cluster
    From previous example:
    cluster A: {1,2,3} => 1,2,3,1,2,3,1,2,3,1,2,3,1,2,…
    cluster H: {1,2,5,8} => 1,2,5,8,1,2,5,8,1,2,5,8,1,2…

## Slide 63: CCC Solution: SOC
Drawbacks
  Inter-cluster communication problem is not solved!
    From the example:
    cluster A: {1,2,3} => 1,2,3,1,…
    cluster E: {2,5,7} => 2,5,7,2,…
    Members in cluster A (e.g. D) cannot communicate with members in cluster E (e.g. E)!
  Which CCC is used for control message exchange in cluster formation (Step 2 & 3)???
B
G
C
A
D
E
H
F
YE={2,5,7}
YH= {1,2,5,8}
YA= {1,2,3}
CD = {1,2,3,5,7}
  CE = {2,3,5,7}

## Slide 64: Swarm Intelligence Based CCC
Swarm Intelligence (SI)
  High efficiency achieved by specialized workers performing specialized tasks in parallel
    Example: ants or bees cooperate to build nests or forage for food
64
T. Chen, H. Zhang, M. D. Katz, and Z. Zhou, “Swarm Intelligence Based Dynamic Control Channel Assignment in CogMesh,” IEEE ICC 2008, May 2008
Notes: 64

## Slide 65: Ant Foraging Analogy to SI-Based CCC
Ant Foraging | CCC Assignment
Each ant individually deposits a small amount of pheromone on a trail | Each CR User sends Hello messages and selects a CCC independently
The trail with the highest pheromone level becomes the choice of the working trail (best route to food) | The best channel selected by most CR users becomes the CCC, fewer CCCs exist in the network
More ants go on the best routes, faster they return with food, and more work achieved overall | More CR users on the same CCC, less control message overheads, faster broadcast, and larger coverage
Efficiency improves because the best routes chosen by majority of ants | System performance improves because of cooperative CCC selection
65
Notes: 65

## Slide 66: Swarm Intelligence Based CCC
Objective of SI-based CCC
  In response to PU activity
    Use the best channel chosen by the majority of CR users as the CCC to increase system efficiency
  In response to CCC coverage improvement
    Reduce the number of CCCs in the network to minimize the control overhead and delay
66
Notes: 66

## Slide 67: Master Channel (CCC) Selection
Channel Quality (a single value Q)
  Quantized quality value Q is obtained from spectrum sensing
  Q = qi for γi ≤ P < γi+1
  The value of Q is inversely proportional to the accumulated interference imposed by surrounding PUs
67
Notes: 67

## Slide 68: Master Channel (CCC) Selection
The Q values are broadcast periodically by HELLO messages
Each node updates its p-List based on Q values of its and neighbor’s master channels
  p-list indicates the probability of a channel selected as the CCC
Master Channel (CCC) Selection
  The channel with the highest probability in p-List
68
Notes: 68

## Slide 69: P list Update
    P list update is based on the difference of Q values in master channels
    Principles
  ∆Q = Qj – Qi > 0 (i.e. neighbor’s Q value is larger)
  The current user increases its Q value of MC
  ∆Q = Qj – Qi < 0 (i.e. neighbor’s Q value is smaller)
  The current user decreases its Q value of MC
69
Notes: 69

## Slide 70: Swarm Intelligence Example
User 1,2,3 with 2 available channels
Assume qi = i, q1: lowest quality, q10: highest quality
  User 1: Q list: {6, 4}
  User 2: Q list: {4, 6}
  User 3: Q list: {8, 2}
Each node constructs initial p list and selects a master channel (MC) based on max p in p list
  User 1: p list: {0.6, 0.4}, MC: Channel 1
  User 2: p list: {0.4, 0.6}, MC: Channel 2
  User 3: p list: {0.8, 0.2}, MC: Channel 1
70
Notes: 70

## Slide 71: Swarm Intelligence Example (2)
User 1 & 3 broadcast Hello messages in Channel 1
  User 1 have two Q lists:
    Its own: Q list {6, 4} and MC = 1
    From user 3: Q list {8, 2} and MC = 1
  User 1: calculate ΔQ = 8-6 = 2 (for MC = 1)
  User 1: update its p list from {0.6, 0.4} to {0.8, 0.2}
  Similarly, User 3 updates p list from {0.8, 0.2} to {0.9, 0.1}
  User 1 & 3 still select Channel 1
User 2 broadcast Hello message in Channel 2
  No one receives this broadcast
71
Notes: 71

## Slide 72: Swarm Intelligence Example (3)
If User 2 next broadcasts Hello message in Channel 1
  User 1 has two Q lists:
    Its own: Q list {8, 2} and MC = 1
    From user 2: Q list {4, 6} and MC = 2
  User 1: calculate ΔQ = 6-2 = 4 (for MC = 2)
  User 1: update its p list from {0.8, 0.2} to {0.7, 0.3}
  User 2:
    Its own: Q list {4, 6} and MC = 2
    From user 1: Q list {8, 2} and MC = 1
  User 2: calculate ΔQ = 8-4 = 4 (for MC = 1)
  User 2: update its p list from {0.4, 0.6} to {0.6, 0.4}
72
Notes: 72

## Slide 73: Swarm Intelligence Example (4)
If User 2 next broadcasts Hello message in Channel 1
  User 3 has two Q lists:
    Its own: Q list {9, 1} and MC = 1
    From user 2: Q list {4, 6} and MC = 2
  User 3: calculate ΔQ = 6-1 = 5 (for MC = 2)
  User 3: update its p list from {0.9, 0.1} to {0.7, 0.3}
Master Channel Update
  User 1: p list = {0.7, 0.3}, MC = 1
  User 2: p list = {0.6, 0.4}, MC = 1
  User 3: p list = {0.7, 0.3}, MC = 1
  All three nodes select Channel 1 as the master channel
73
Notes: 73

## Slide 74: CCC Solution: Swarm Intelligence CCC
Advantages
  PU activity protection and CCC coverage improvement
    Adaptive CCC selection by the majority increases robustness to PU activity on the selected CCC
    CCC coverage increases as the number of CCCs reduced
74
Notes: 74

## Slide 75: CCC Solution: Swarm Intelligence CCC
Drawbacks
  Accuracy of Q value as PU activity indicator
    Q and p values may not accurately reflect true PU activity
  Control overheads
    Frequent HELLO broadcasts contribute to control overheads
    Broadcast rate needs to be controlled
  Slow converging rate and response to dynamic PU activity
    Speed of responding to PU activity is a concern
    Ping pong effect may occur as a result of neighbors with different MC selections
75
Notes: 75

## Slide 76: Underlay CCC Solutions
Underlay CCC by UWB Communications
  Control messages modulated on spreading sequences
  Transmitted in low power as short pulses
  Exhibit an ultra wide signal bandwidth compared to channel bandwidth
  Appear to PUs as noise
  No harmful interference with the PU traffic in licensed data channels
Narrowband licensed data channels
UWB CCC
f
A. Masri, C.-F. Chiasserini, and A. Perotti, “Control information exchange through UWB in cognitive radio networks,” IEEE International Symposium on Wireless Pervasive Computing, ISWPC’10, 2010

## Slide 77: Issues in UWB CCC Design
UWB transmissions are known to have short transmission range
Two Issues Related to UWB transmission range
  How to increase the limited transmission range
    Spreading code may be utilized to increase the range
  How to resolve the range difference between the UWB control radio and other type of data radio
    A neighbor that can be reached by the data radio in one hop may not be reachable by the UWB radio

## Slide 78: UWB CCC Solution
UWB CCC with Multi-hop Control Routing
  Address the range difference issue
  CCC routing table is established during neighbor discovery for routing control packets to all neighbors
  Intermediate nodes between source and destination forward control packets back and forth to complement the difference between control and data radio ranges

## Slide 79: UWB CCC and Range Difference Example
RUWB and RWLAN represent the transmission range of UWB radio and WIFI radio
CR users B and C are both one-hop UWB neighbor and one-hop WLAN neighbor of A
CR users D and E are one-hop WLAN neighbor but not reachable by UWB radio of A
Intermediate node (CR user C) needs to forward control packets back and forward between CR users A and D

## Slide 80: CCC Solution: UWB CCC
Advantage
  Robust to PU activity and jamming
Drawbacks
  Short transmission range (small CCC coverage)
  Range difference issues if different radios are used
  Control overhead increase with the multi-hop control routing

## Slide 81: Our CCC Solutions
Dedicated CCC Solution
  OFDM-based common control channel design
In-band CCC Solution
  Efficient recovery control channel (ERCC) design

## Slide 82: OFDM-based Common Control Channel
“Always-on” dedicated CCC Solution
  Utilize the white space in guard bands
  Select OFDM subcarriers in guard bands as CCCs
K. R. Chowdhury and I. F. Akyildiz, “OFDM-based common control channel design for cognitive radio ad hoc networks,” IEEE Trans. Mobile Computing, vol. 10, no. 2, Feb. 2011.

## Slide 83: OFDM-based CCC: Motivation
Guard bands are always available
  Using them minimizes the disruption to an ongoing CR data transfer and to a newly arriving PU
Guard band may be allotted a large total bandwidth
  Using them makes efficient use of the scarce spectrum resource

## Slide 84: OFDM-based CCC Design Steps
Step1: OFDM Subcarrier Allocation
  Use optimization framework for network initialization
  Select OFDM subcarrier and transmission parameters
    Number of subcarriers per guard band (m), symbol time (τ), transmit power (Ptx)
Step 2: CCC Operations
  Select center subcarriers for broadcast messaging
  Select active guard bands for unicast messaging
  Use learning framework for normal network operations

## Slide 85: OFDM Subcarrier Allocation
OFDM-based Subcarrier Optimization Framework
Orthogonality
GB Bandwidth
Peak to Avg. Power Ratio (PAPR)
Tx range
Data rate
Tx time
Interference
Constraints:

## Slide 86: CCC Operations: Broadcast Messaging
Message Broadcast on CCC
  Broadcast facilitates higher layer operations
  Examples of broadcast messages
    Cooperative decision sent by the fusion center in cooperative sensing
    Hello packet exchange during neighbor discovery
    RTS-CTS handshake at the link layer
    Route request packets sent at the network layer
   Broadcast messages may interfere with ongoing PU transmissions outside the immediate sensing range

## Slide 87: CCC Operations: Broadcast Messaging
All center subcarriers are utilized for broadcast
  Central subcarrier of a guard band has the largest frequency separation between itself and adjacent PU spectrum
For Broadcast

## Slide 88: CCC Operations: Unicast
PU activity affects the choices of active guard bands
Multi-armed bandit algorithm is used to learn the best combination of active guard bands over time
  Exploit the current choice of the arm and get the known level of immediate reward
  Explore a new arm to get potentially higher expected reward in the long run

## Slide 89: Unicast: Multi-Armed Bandit Algorithm
Rules of Creating Arms
  A guard band (GB) is active if all subcarriers in it are used
  Center subcarriers are always used
  An arm is a combination of GBs
  Ex: 3 GBs: 23 = 8 possible arms

## Slide 90: Bandit Algorithm: Step 1
Initialization:
  Set weights wi(t) = 1 for i = 1,…,K
Step 1: Choosing the Arm
  Probability of choosing each arm pi(t):
    Tuning parameter γ helps decide the arm selection probability as a function of their weight:
    Set g = number of rounds of the arm selection
  CR user s sends packet PKTq to intended receiver r on the CCC by selection of the qth arm

## Slide 91: Bandit Algorithm: Step 2
Step 2: Assigning the Reward
  Receiver r receives PKTq and identify the set of I
    I: Set of subcarriers whose signal power exceeds interference threshold
  Reward assigned by the receiver Rc:
    ν: number of guard bands used for the qth arm
    m: number of carriers in a guard band
    Ng: number of guard bands
    1st term: fractional number of interference-free subcarriers
    2nd term: the ratio of current data rate to maximum possible data rate
  Receiver r sends ACK packet with reward Rc back to CR user s by broadcast

## Slide 92: Bandit Algorithm: Step 3
Step 3: Updating Arm Selection Probability
  Receiver receives PKTq and identify the set of I
  Weight update:
    Scaled reward:
Go back to Step 1:
  For the next packet sent by the CR user s, the new weights are used in order to calculate the probabilities of choosing arms pi(t)

## Slide 93: OFDM-based CCC: Performance Metrics
Broadcast Messaging
  Interference with PUs
  Spectrum utilization efficiency
  Throughput
Unicast Messaging
  Spectral interference
  Fairness of subcarrier selections
  Rewards

## Slide 94: Broadcast Performance: Interference with PUs
Interference-Time Product Ω
  Product of interference caused to PUs and the time for which this interference in effect
    Cluster (SI-based): the preference of neighbors outside PU range outweighed the choice of the CR user, leading to higher local interference
    Sequence (Seq Rendezvous): each CR user must successively synchronize with all neighbors in turn, leading to high Ω

## Slide 95: Broadcast Performance: Spectrum Efficiency
Spectrum Utilization Efficiency
  Measure the ratio of time spent in useful transmission to total time needed
    O-CCC: gradual decrease with no. of users due to guard time per OFDM symbol (to reduce multipath effect)
    Cluster: several rounds of message exchange before a CCC is determined
    Sequence: lowest utilization due to channel hopping in discrete intervals
      Next channel is switched only after current hopping duration is completed

## Slide 96: Broadcast Performance: Throughput
Average Broadcast Throughput
  For scenarios in which messages are forwarded over 10 hops
    O-CCC: only a limited number of central subcarriers exist, lowering effective link bandwidth and end-to-end data rate
    O-CCC lower than Cluster
    Sequence: long synchronization time at each hop lowers the throughput significantly over multiple hops

## Slide 97: Unicast Performance: Spectral Interference
Spectral Interference
  Schemes for comparison
    CCC-Bandit: using bandit algorithm
    CCC-All: all subcarriers activated
    O-CCC: the broadcast scheme
  CCC-Bandit
    Interference of CCC-Bandit is bounded between that of other two schemes
    Low percentage increase in interference
    For a given PU occupancy, CCC-Bandit dynamically converges on the best set of guard bands

## Slide 98: Unicast Performance: Fairness of Selections
Fairness of Subcarrier Selections
  Spectrum opportunity Г: number of trials undertaken for each arm
    Most of the arms lie in the range of 1/3 to 2/3 of the maximum possible Г
    Outliers are very limited
2 occupied PU channels
6 occupied PU channels

## Slide 99: Unicast Performance: Rewards
Cumulative Rewards
  Convergence to the best channel is slow when number of affected channels is small (Top Fig.)
    Higher rewards being accumulated by several different arms
  Convergence to the best possible combination is speeded up as number of affected channels increases (Bottom Fig.)
    Most of the arms incur a reward lower than 2
    Very few arms with maximum reward earned
The procedure identifies the best arm combination over time and exploits it over the others
2 occupied PU channels
6 occupied PU channels

## Slide 100: Efficient Recovery Control Channel (ERCC)
Heuristic Distributed CCC Solution
  Establish and maintain a common channel list (CCL)
  Exchange CCL with neighbors
  Utilize CCL for recovering CCC if current one occupied by PUs
Design Goals
  Responsiveness to PU activity
  Improved CCC coverage
  Reduced overhead for CCC establishment
B. F. Lo, I. F. Akyildiz, and A. M. Al-Dhelaan, “Efficient recovery common control channel design in cognitive radio ad hoc networks,” IEEE Trans. Vehicular Technology, vol. 59, no. 9, Nov. 2010.

## Slide 101: ERCC: Motivation
Channel Availability
  CR users in a neighborhood observe similar channel availability
Common Channels
  Finding common channels is similar to finding longest common subsequences
CCC Recovery
  Efficient recovery from PU activity can be achieved with well-designed and updated common channel lists and neighbor information

## Slide 102: ERCC in Actions
Neighbor Discovery
  Establish initial network topology and CCL
  Establish connection in case of losing neighbors due to PUs
Common Channel List Update
  Update channel and neighbor information regularly with local and neighbor’s channel availability
Efficient CCC Recovery from PU Activity
  Recover the majority of neighbors efficiently by using common channel list

## Slide 103: ERCC: Neighbor Discovery
Channel Hopping for Neighbor Discovery
  Neighbors rendezvous on common channels of good channel quality in the neighborhood with higher probability
  Neighbor pair exchanges common channel list after rendezvous
Algorithm
  Sequence generated from uniform distributed random numbers
    Common channel list LC of length n
    Probability of selecting Ci:
    Value of CDF at C=Ci is FC(Ci)
    Given a sequence of random numbers rm, m=1,2,…
    Sm = Ci for FC(Ci-1) < rm ≤ FC(Ci)

## Slide 104: Example: Neighbor Discovery and Initial Network Topology
10 PUs, 60 CR users, 10 channels, one PU per channel
PU Tx range 200m, CR user Tx range 100m
PU 8 on Ch 1
PU 7 on Ch 2
CR Users on Ch 2
CR Users on Ch 1

## Slide 105: ERCC: Common Channel List Update
Advantages of Common Channel List
  Selecting the channel common to the largest number of neighbors as the control channel increases CCC coverage
  When a PU occupies the current CCC, the common channel with the highest preference from the list can be immediately allocated as the new control channel

## Slide 106: ERCC: Common Channel List Update
Update with Local Sensing Information
  PU activity affects channel availability
    Channels in the list may be no longer available
    New channel opportunities may be available
  Periodic local sensing to obtain latest channel availability
Update with Neighbors’ Information
  Determine a list of common channels shared with neighbors
  Collect and combine neighbors’ common channel preference for dissemination of CCC candidates

## Slide 107: ERCC: Common Channel List Update
Update with Sensing Information
  Obtain a preferred channel list LP from spectrum sensing
    LP is a channel list of observed quality in monotonically decreasing order
  Add new available channels
  Remove channels no longer available
  Example: Figure (a)
    Compare a Lp to a CCL LC
    Ch3 is no longer available
    Ch8 is newly available
    Note that the order is preserved in the updated list

## Slide 108: ERCC: Common Channel List Update
Update with Neighbor’s Information
  Broadcast local CCL and receive CCL broadcast from neighbors
  Find the largest number of common channels from two CCLs
  Sort new list based on channel weights and channel quality (interference level)
    Channel weight (w): Number of neighbors reached by the channel
    Channel quality: Conversely proportional to accumulated interference with surrounding PUs
  Example: Figure (b)
    LC1 is local and LC2 is from a neighbor
    Ch3 & Ch7 are locally available
    They are included in the list for broadcast
w1: 3 3 2 1 1
w1: 2 2 1 1 1
w2: 2 2 1 1 1

## Slide 109: ERCC: Efficient Recovery from PU Activity
PU’s Return to CCC
  Example: Figure (b)
    CCC is Ch 1 between CR user 1 and 2
    PU returns to Ch1
    Both CR users 1 & 2 change CCC to Ch2 without communicating with each other
    CR users 1, 2, and others rendezvous on Ch 2
    Most neighbors are recovered on Ch2 immediately
w1: 3 2 1 1

## Slide 110: ERCC Performance Metrics
CCC Link Indicator (CLI)
  Percentage of CCC links over all available links
  Indicate how fast CR users establish links with new neighbors and recover links with old neighbors
  Evaluate neighbor discovery rate and the responsiveness to PU activity
CCC Coverage Indicator (CCI)
  Normalized standard deviation of control channel distribution over all licensed channels
  Indicate the footprint of CR users sharing a CCC
    CCI achieves unity when all CCC links in the network are established in the same channel

## Slide 111: ERCC Performance Metrics
Best Channel Indicator (BCI)
  Percentage of CCC links to which the best quality channel observed at each CR user is allocated
  Indicate the quality and reliability of CCC selections
Average PU Interference Level (PUI)
  Average accumulated interference from PUs on the CCC
  Indicates the average level of interference from PUs per SU during control transmission
    Higher PUI implies higher possibility of PU activity in surrounding areas
  Evaluate the level of achievable control throughput
    The higher the PUI level, the lower the control throughput

## Slide 112: ERCC Performance Evaluation
Test Cases
  PU ON/OFF period
  PU transmission range
  PU density as the number of PUs per channel
  SU transmission range
  Scalability or density of SU population
  Shadow fading for a range of decibel spread
Comparison
  GRP: Swarm intelligence-based CCC assignment
  SEQ: Sequence-based rendezvous

## Slide 113: ERCC Test Case: PU ON/OFF Period
CCC Link Indicator (CLI)
  ERCC: above 0.8 and close to 1 for medium and low PU activity
  GRP: at most 0.8
  SEQ: low CLI values
CLI shows Strengths of ERCC
  Maintain network connectivity under PU activity
  Recover CCC efficiently upon PU’s return to CCC

## Slide 114: ERCC Test Case: PU ON/OFF Period
CCC Coverage Indicator (CCI)
  For high PU activity, GRP has higher CCI than ERCC
  For medium and low PU activity, ERCC outperforms GRP
  SEQ has considerably low CCI value
ERCC
  Better balance between coverage and interference avoidance than GRP
  Extend the coverage with the selection of higher quality CCC

## Slide 115
Best Channel Indicator (BCI)
  For high PU activity, ERCC and SI are comparable
  For medium and low PU activity, ERCC outperforms SI
  SEQ has considerably low BCI value
ERCC
  Higher quality CCC selection for increasing coverage and reducing interference
ERCC Test Case: PU ON/OFF Period

## Slide 116: ERCC Test Case: PU ON/OFF Period
PU Interference (PUI)
  ERCC: Consistently low interference with PUs
  GRP and SEQ cause significantly higher interference
ERCC
  Less susceptible to PU’s interference
  Balance among robustness to PU activity (CLI), broadcast operations (CCI), CCC reliability (BCI), PU protection and control throughput (PUI)

## Slide 117: CCC Research Challenges
Sequence-based CCC Challenges
  Hopping Sequence design for PU activity and CCC coverage
    Existing schemes react to PU activity after sequences are constructed
    Existing designs seldom consider control broadcast in hopping sequences
Group-based CCC Challenges
  Effective intergroup communications
    Without reliable inter-group communications, CR network may be partitioned into isolated groups
  Efficiency of regrouping
    Regrouping efficiency are crucial to the responsiveness to PU activity
117
B. F. Lo, “A survey of common control channel design in cognitive radio networks,” Physical Communication (Elsevier) Journal, vol. 4, no. 1, March 2011.
Notes: 117

## Slide 118: CCC Research Challenges
UWB CCC Challenge
  Spreading code design for range-rate tradeoff
    Spreading code can be utilized to group CR users for cooperation and balance the tradeoff between range and data rate
    Required control message rate may be compromised by the spreading sequences for enlarging transmission range
Control Channel Security Challenge
  Impact of Jamming on PU Activity
    PUs are also under attack when CR users are attacked
    CCC challenges when PU activity changes due to jamming
118
B. F. Lo, “A survey of common control channel design in cognitive radio networks,” Physical Communication (Elsevier) Journal, vol. 4, no. 1, March 2011.
Notes: 118